Libre Space Foundation
SLIDE 1

---
Libre Space Foundation
SLIDE A

---
Open Source Ground Station Network
by Alfredos Damkalis
[Speaker Notes: 10q 10q Remind them for Satnogs demo QnA]

---
What is SatNOGS Project?
A network of ground stations
Open Source (Hardware, Software, Data)
Modular Design
Automate Satellite Communications

---
What is SatNOGS Project?
Ground Station
Client
gr-satnogs
Rotator
Web and other Services:
Network
DB
Decoders
Dashboard

---
Ground Station - SatNOGS Client
Handles Ground Station – SatNOGS Network communication
Performs and co-ordinates observations
Installation from source, python package or ansible script in Linux.
Reference setup uses ansible script coming with ready-to-flash Raspberry Pi Image for RPi3 or RPi4

---
Ground Station - SatNOGS Client
The last year:
Added support for new
gr-satnogs scripts
Several bug fixes
Improved codebase
Release of v1.0
Future:
Continue implementation of the new architecture
Support transmission under SatNOGS COMMS project

---
Ground Station - gr-satnogs
SatNOGS GNU Radio Out-Of-Tree Module
Process and demodulate received signal
Installation from source, package or ansible script in Linux.
Reference setup uses ansible script coming with ready-to-flash Raspberry Pi Image for RPi3 or RPi4

---
Ground Station - gr-satnogs
Modes supported by gr-satnogs flowgraphs:
CW
APT
DUV
APRS1200 and APRS9600
IEEE 802.15.4
BPSK(1200-19200)
FSK(1200-19200)
MSK(1200-19200)
AFSK(1200-9600)

---
Ground Station - gr-satnogs
The last year:
Improved flowgraphs performance
Added new flowgraphs
Moved packaging to
Open Build Service
Added gr-soapy support
Future:
More improvements on flowgraphs performance
Transition from gr-osmosdr to gr-soapy
Support transmission under SatNOGS COMMS project
Metadata support for data frames

---
Ground Station – SatNOGS Rotator
Hardware and Firmware components of a Rotator
Moves directional antennas to aim satellites passes
Detailed documentation in wiki.satnogs.org

---
Ground Station – SatNOGS Rotator
Azimuth – Elevation or X – Y Type
16NM continuous torque (5kg antenna load)
1 deg pointing accuracy
0.04 deg measurement accuracy
RS485(EasyComm3) interface, 48V at 1A
Weather-proof - Operational at 5-40 °C
Electromagnetically Shielded
Wind Sustained 29-38 km/h

---
Ground Station – SatNOGS Rotator
The last year:
Release of v3.1
Several fixes and improvements
Extended Testing
More users inside and outside SatNOGS Network
Future:
Continue Testing and improvements
Development of and updates on hardware components useful for ground stations, like diplexers, amplifiers and filters

---
Web & Other Services – SatNOGS Network

---
Web & Other Services – SatNOGS Network
Network station management
Station/Satellite scheduling
Observation results collection and display

---
Web & Other Services – SatNOGS Network
220 Online Stations
110 Testing Stations

---
Web & Other Services – SatNOGS Network
~3000 Observations/Day
~9000 Demodulated Data/Day

---
Web & Other Services – SatNOGS Network
From 2017-08 until 2018-09
From 2018-09 until 2019-09

---
Web & Other Services – SatNOGS Network
ARISS – SSTV event April 2019:
Total duration of the event:
3d 34min 58s (announced ~3d)
Total coverage (with or without decoded data):
1d 2h 25min 52s
~36.42% of the total event time
Total coverage (with decoded data):
8h 45min 26s
~12.07% of the total event time
Total time of observations
(includes overlapped observations):
7d 19h 9min 22s

---
Web & Other Services – SatNOGS Network
The last year:
Refactored Observation Scheduling
Scheduling API
Scheduling Automation
Several fixes and performance improvements
Reached 1 million observations!!!
Future:
Move to Python 3 and Django 2
Improve API
Release API client
Move from waterfall image to waterfall data
Support transmission under SatNOGS COMMs project

---
Web & Other Services – SatNOGS DB
Crowd-sourced satellite/transmitters database
Repository for collected telemetry and payload frames

---
Web & Other Services – SatNOGS DB
383 Satellites
785 Transmitters
654 Contributors collected more than 48.5 million frames
SatNOGS Network
DK3WN TLM Forwarder
Gr-satellites sids forwarder

---
Web & Other Services – SatNOGS DB
The last year:
Moved to Python 3 and Django 2.x
Improved codebase
Several fixes and performance improvements
Future:
Improve API
Realease API Client
Integrate MetaSat Schema
Provide better statistics
Improve and automate frames validation

---
Web & Other Services – SatNOGS Decoders
Collection of kaitai.io structs
Describe encoding of satellite dataframes
Structs are used to generate python decoders

---
Web & Other Services – SatNOGS Decoders
Supported Decoders
AAUSAT4
ACRUX-1
ARMADILLO
AMSAT FOX DUV
AX.25 frame decoder
CAS-4A & CAS-4B
CHOMPTT
CubeBel-1
Elfin-A & Elfin-B
Entrysat
Lightsail-2
QBEE
Siriussat-1 & Siriussat-2
skCUBE
Strand-1
TBEX-A/TBEX-B
Unisat-6

---
Web & Other Services – SatNOGS Decoders
The last year:
New Decoders
Improved codebase
Several fixes and performance improvements
Future:
More decoders to come
Involve more people/satellite teams before their satellite deployment

---
Web & Other Services – SatNOGS Dashboards
Collection of satellite dashboards in Grafana Environment
Display/Visualize decoded data from satellite data frames

---
Web & Other Services – SatNOGS Dashboards
The last year:
New Dashboards created by the community and satellite teams
Satellite teams used dashboards for mission analysis
Future:
More dashboards to come
Involve more people/satellite teams before their satellite deployment

---
THANK YOU!
SatNOGS COMMUNITY

---
Join us
Wiki: https://wiki.satnogs.org
Repos: https://gitlab.com/librespacefoundation/satnogs
Community: https://community.libre.space
Thank you!